## Slide 1
DEEP LEARNING FOR SURGICAL ROBOTICS
AI-Assisted
Robotic Surgery
Instrument Detection, Tissue Segmentation, and Autonomous Motion Planning
with Deep Learning, ROS 2, and Gazebo Simulation
EndoVis2017 Dataset
U-Net Segmentation
YOLO Detection
ROS 2 Integration
Deep Learning & Robotics Capstone Project

## Slide 2
INTRODUCTION
Introduction to AI-Assisted Robotic Surgery
Robot-assisted surgery gives surgeons precision, stability, and minimally invasive access, but the surgeon still carries the full cognitive load of identifying instruments, tissue boundaries, and safe motion paths in real time.
This project explores how deep learning can augment that workflow — automatically detecting surgical instruments, segmenting tissue and target regions, and feeding that understanding into a ROS 2-controlled robotic pipeline.
The result is a closed loop: perception models interpret the surgical scene, and that interpretation informs motion planning and control — a step toward safer, more autonomous surgical assistance.
Why It Matters
Precision
Sub-millimeter awareness of instrument and tissue position
Consistency
Reduces variability from fatigue or limited visibility
Autonomy Pathway
Foundation for semi-autonomous surgical assistance
Safety
Real-time perception enables collision-aware motion control
AI-ASSISTED ROBOTIC SURGERY
02

## Slide 3
OVERVIEW
System Architecture
From raw endoscopic video to closed-loop robotic control
Data
EndoVis2017
surgical video &
segmentation masks
→
Deep Learning
U-Net segmentation +
YOLO instrument
detection
→
ROS 2 Node
Publishes inference
results on
dl_project_status
→
Gazebo Sim
Virtual surgical
environment for
safe testing
→
Robot Control
Motion planning &
instrument-aware
actuation
Closed feedback loop — perception continuously informs control
AI-ASSISTED ROBOTIC SURGERY
03

## Slide 4
TECHNOLOGY STACK
Deep Learning + ROS + Gazebo
Three technologies, one integrated surgical intelligence pipeline
Deep Learning
The Perception Layer
U-Net segments tissue & instruments pixel-by-pixel
YOLO localizes instruments with bounding boxes
Trained on 1,800+ annotated EndoVis2017 frames
+
ROS 2
The Communication Layer
Wraps trained models into a live inference node
Publishes results on standardized topics
Bridges perception output to robot controllers
+
Gazebo
The Simulation Layer
Physics-accurate virtual surgical environment
Safe space to test motion before real deployment
Validates the full perception-to-control loop
AI-ASSISTED ROBOTIC SURGERY
04

## Slide 5
APPLICATION
Role of Deep Learning in Robotic Surgery
Scene Perception
Continuously interprets endoscopic video to identify instruments, tissue, and anatomical landmarks in real time.
Instrument Awareness
Detects instrument position and orientation, enabling collision avoidance and precise tool tracking.
Tissue Differentiation
Pixel-level segmentation distinguishes target tissue from background and critical structures.
Motion Guidance
Perception output constrains and informs the robot's planned trajectories for safer movement.
Risk Reduction
Flags ambiguous or low-confidence regions, supporting the surgeon rather than replacing judgment.
Continuous Learning
Model performance is measured and refined against clinical-grade accuracy benchmarks.
AI-ASSISTED ROBOTIC SURGERY
05

## Slide 6
SIMULATION
Gazebo-Based Surgical Environment Simulation
Why Simulate First?
Before any perception or control logic reaches a physical robot, it is validated inside Gazebo — a physics-based 3D simulator integrated directly with ROS 2.
Zero-risk testing of motion planning logic
Rapid iteration without hardware constraints
Reproducible scenes for consistent evaluation
Direct bridge to ROS 2 topics used in deployment
Simulation-to-Deployment Loop
Build virtual OR scene
Instruments, tissue models, and camera views defined in Gazebo
Spawn robot model
URDF-defined manipulator matches real robot kinematics
Feed DL perception
U-Net & YOLO outputs stream into the simulated control loop
Validate & tune
Motion paths verified for safety before real-world transfer
AI-ASSISTED ROBOTIC SURGERY
06

## Slide 7
DATA ENGINEERING
Synthetic Data Generation
Deriving detection labels directly from segmentation masks
EndoVis2017 ships with pixel-level segmentation masks but no bounding-box labels. To train the YOLO detector without manual annotation, bounding boxes are synthetically generated by locating the foreground pixels of each instrument class and computing their enclosing rectangle — producing a complete detection dataset directly from existing segmentation labels.
1. Segmentation Mask
Start from ground-truth
pixel labels (0–7 classes)
→
2. Isolate Foreground
Identify non-background
pixels per instrument
→
3. Compute Min/Max X, Y
Derive the tightest
enclosing bounding box
→
4. Synthetic YOLO Label
Auto-generated annotation
ready for detector training
AI-ASSISTED ROBOTIC SURGERY
07

## Slide 8
PERCEPTION · DETECTION
Surgical Instrument Detection Using YOLO
SIMULATED DETECTION OUTPUT
instrument_1 0.94
instrument_2 0.89
Illustrative rendering — bounding boxes derived from EndoVis2017 masks
Weakly-Supervised Detection Pipeline
No manual boxes needed
Bounding boxes are derived directly from existing segmentation masks — no separate detection annotation pass.
One box per instrument region
Each connected foreground region in a frame is treated as a distinct instrument to localize.
Real-time inference target
The trained detector is designed to run inside the ROS 2 node alongside the U-Net segmenter.
Feeds motion planning
Detected instrument location and confidence pass downstream to the control layer.
AI-ASSISTED ROBOTIC SURGERY
08

## Slide 9
PERCEPTION · SEGMENTATION
Tissue and Target Segmentation Using U-Net
U-Net Encoder–Decoder Architecture
512²
256²
128²
64²
Encoder (downsampling)
Decoder (upsampling)
Training Configuration
Loss function
Combined BCE + Dice Loss for pixel-level class balance
Optimizer
Adam, updating U-Net weights each training step
Precision mode
Mixed-precision (AMP) training, optimized for RTX 3050
Task
Binary foreground/background surgical instrument masks
AI-ASSISTED ROBOTIC SURGERY
09

## Slide 10
INTEGRATION
Integrated DL Model with ROS 2
Wrapping trained perception models into a live robotic node
deep_learning_node
ROS 2 Node (rclpy)
1
U-Net performs pixel-level segmentation on the incoming frame
2
YOLO detector localizes surgical instruments in parallel
3
Node publishes a status message on the dl_project_status topic
4
Downstream ROS 2 nodes subscribe for motion planning input
Live Node Output
$ ros2 run dl_pipeline deep_learning_node
[INFO] [deep_learning_node]: U-Net segmentation + YOLO
detection completed
Topic: /dl_project_status → String msg
Why This Matters
Decouples model inference from robot control logic
Standard ROS 2 topics make the perception layer reusable
Same node architecture transfers from Gazebo to real hardware
AI-ASSISTED ROBOTIC SURGERY
10

## Slide 11
CONTROL LAYER
AI-Based Robot Motion Planning and Control
Turning perception into safe, deliberate robot movement
Perceive
U-Net + YOLO outputs describe instrument
and tissue positions each frame
→
Interpret
Detections mapped to robot-frame
coordinates for planning
→
Plan
Candidate trajectories generated,
respecting no-go tissue zones
→
Act
Selected motion sent to the robot
controller via ROS 2
Core Control Principles
Constraint-aware planning around segmented tissue
Confidence-gated actuation — low-confidence detections defer to the surgeon
Every planned motion validated first in Gazebo simulation
AI-ASSISTED ROBOTIC SURGERY
11

## Slide 12
EVALUATION
Results and Evaluation Based on Accuracy
U-Net segmentation performance on the EndoVis2017 validation set
93.17%
Dice Score
87.22%
IoU
92.43%
Precision
93.93%
Recall
Chart: Segmentation Metrics
| Dice | IoU | Precision | Recall
Score (%) | 93.17 | 87.22 | 92.43 | 93.93
Project Summary
Best validation loss
0.1744
Training samples
1,800 frames
Validation samples
901 frames
YOLO detection
Implemented
ROS 2 integration
Completed
PROJECT STATUS: COMPLETED
AI-ASSISTED ROBOTIC SURGERY
12